## Slide 1: FRC Java Lesson 4 Programming the Robot Kyle Spurlock Team 313 Bionic Zebras

## Slide 2: Starting a new Project
1. In NetBeans, go under File and click on New Project.
2. Click on the FRC Java Category.
Under Projects, there are a list of templates: Command Based, Interative Robot, and Simple Robot. Each of them can be used to program the robot in different ways for certain functionalities.
3. Select the Simple Robot Template and click Next.

## Slide 3: Naming your Project
1. Under Project Name, name it My First Robot Program, or something along those lines.
2. Don't change anything else and press Finish.

## Slide 4: My First Robot Program
On the left side of the screen, there should be something called My First Robot Program. You will see two things called src and build.xml. Click on the plus next to where it says src. Now press the plus for the long name that popped up under it. Finally, double-click on RobotTemplate.java. This is where you will be writing your code.

## Slide 5: What do these functions do?
Starting from the top (the important ones):
RobotTemplate extends Iterative
- This is where all of the variables are declared so they can be used later in teleop and autonomous.
autonomousPeriodic()
- Code in this function happens once: the moment when a match begins, which is when the robot moves based on programmed commands.
teleopPeriodic()
- This is called after autonomous when the driver and operator control the robot based on programmed buttons and joystick axes.

## Slide 6: Initialization
Under the class RobotTemplate, the drive mode, joysticks, motor controllers, relays, sensors, and the compressor are all set up using a special type of variable using this:
<type> <name> = new <type>(<param>);
Drive mode looks like this:
RobotDrive robotDrive = new RobotDrive(1, 2, 3, 4);
- The parameters depend on the type of object you declare, with this being the PWM numbers for each wheel they control.

## Slide 7: Initialization: Drive and Joysticks
There are three main types of drive modes: Tank Drive, Arcade Drive, and Mecanum Drive.
We'll be focusing on Tank Drive, where there are two joysticks: left controls left wheels and right joystick controls right wheels.
The Joystick is declared like so:
Joystick leftJoystick = new Joystick(1);
Joystick rightJoystick = new Joystick(2);
For this variable, there is only one parameter: the USB slot the joystick is plugged into the driver station.
Any other sort of other controller is still declared the same way as a joystick.

## Slide 8: Initialization: Importation
Getting this far, you may have noticed the somewhat annoying red underline on RobotDrive and Joystick, which is showing that there are errors.
To fix this, we need to import these new variable types that NetBeans doesn't recognize yet.
This can simply be fixed by pressing Shift-Ctrl-i
Notice that there are new imported files.

## Slide 9: OperatorControl()
We're moving down to operatorControl() so we can get the robot to move.
Type this on one line inside operatorControl() and press enter.
while (isOperatorControl() && isEnabled()) {
This checks to see if the robot is on and that it's running teleop. Put this line after:
robotDrive.tankDrive(leftJoystick, rightJoystick);
This sets up the tank drive to use the left and right joysticks for moving the robot's wheels.